## Slide 1: AF NC3 CENTER
Mr. Jonathan Wilson AFNC3C
AF NC3 Weapons System
Mission Performance Brief
October 2019
Notes: Good Day ???,
Welcome to the NC3 Mission Performance Briefing for November, 2019.

## Slide 2: NC3 MPI Dashboard
FUNCTIONAL GROUP | NC3 SENIOR LEADER COMMS |  | NC3 PRIMARY CONTROL CENTERS & SENSORS |  |  | AF NUCLEAR DELIVERY SYSTEMS |  |  |  | NUCLEAR SUPPORT AND RECOVERY TEAM |  | 
CONFIG ELEMENT | VC-25 NC3 SLC | EA NC3 SLC | ABN NC3 SLC-CC | Fixed PCC SENSOR | Trans PCC SENSOR | B-52 NC3 | B-2 NC3 | DCA NC3 | ICBM NC3 | ABN NC3 SUPT | Fixed NC3 SUPT | Mobile NC3 SUPT
Airborne PCC CE (E-4B)
Airborne Delivery CE (B-52H)
Airborne Delivery CE (B-2)
Airborne Delivery CE (F-15E)
Delivery CE (ICBM)
Airborne Support CE (U-2) (K/RC-135)
Fixed Support CE
Trans PCC Sensor CE
Fixed PCC Sensor CE
Mobile Support CE
SLC CE
EA CE
Weapons System Configuration Elements (CE)
Denotes some data captured but not fully mature
Notes: Sir, the NC3 Dashboard depicts the AF NC3 WS (AN/USQ-225) Configuration Elements (CE’s). The CE’s with check marks/highlighted will be briefed, the CE’s not checked for this iteration and will become available as data mining matures. The NC3 MPI is structured to show performance indicators of NC3 Systems that reside within/on the CE’s. This iteration of the NC3 MPI Brief will capture the Airborne PCC (E-4B) CE,
B-52H CE, B-2 CE, DCA CE, Airborne Support CE (U-2), ICBM CE and Fixed Support CE.
1. In this brief we will be addressing constituent systems for each Configuration Element as; GREEN meaning the system has met all standards OR if the system has not met ONLY one standard within the lagging and/or leading indicators, and RED meaning the system did not meet two or more standards within the lagging and/or leading indicators.
2. For slide justification purposes, the "Red" indicated systems will be explained further with an issue slide. Those issue slides will be accompanied by that specific systems’ lagging and leading indicator charts themselves.

## Slide 3
Airborne PCC (E-4B) CE SCORECARD
E-4B (AN/ASC-46) CE SCORECARD FY-19
2nd Quarter 19 |  |  | QTD
3rd Quarter 19 |  |  | QTD
YTD
99.93
0.89
0.06
569
7
Rate | Avg | 1st Quarter 19 |  |  | QTD
MC | 99.30 | 99.93 |  |  | 99.93
TM | 3.80 | 0.89 |  |  | 0.89
TS | 5.50 | 0.06 |  |  | 0.06
MTBF | 424 | 569 |  |  | 569
MDT | 64 | 7 |  |  | 7
- USC-42 (UHF SATCOM) - AAR-88 (MMRT, LF/VLF)
- USC-28 (SHF VOICE) - ARC-210 (UHF)
- SECN (EHF VOICE) - ARC-208 (MILSTAR)
- NPES (SOFTWARE) - ARC-190 (HF)
- MPS (SOFTWARE) - ARC-171 (UHF)
- ACS-24 (SHF SATCOM)
4rd Quarter 19 |  |  | QTD
Notes: AIRBORNE CC (E-4B) NC3 Availability Chart
Good morning ???, I am Mr. ??? from the NC3 Center and I will be briefing the Airborne PCC (E-4B) Configuration Element (CE) Maintenance Performance Indicators.
Scoreboard Indicators:
The combined Airborne (E-4B) PCC CE Mission Capability rate takes into account the USC-42, USC-28, SECN, NPES, MPS, FDMA, ASC-24, ARR-88 (MMRT) ARC-210, ARC-208, ARC-190, ARC-183 (DTWA) and ARC-171 individual systems.
The overall E-4B Configuration Element met 5 of 5 reported maintenance indicators for the Year To Date and Quarter To Date average. All standards were established by importing 24 months
of data into a standards development workbook, first up is the Mission Capability (MC) rate.
The monthly and quarterly data is color coded with either Green for Fully Mission Capable (FMC), Yellow for Partially Mission Capable (PMC), or Red for Non-Mission Capable (NMC). These color codes are categorized using the following parameters:
Green - At or less than 3% variance from the average
Yellow - Between 3-5% variance from the average
Red - Greater than 5% variance from the average
This goes for all categories except for Total Supply Downtime (TS), which use <10%, 10-15%, and >15% respectively.
MC Rate :
MC rate is a percentage that is either Fully Mission Capable (FMC) or Non-Mission Capable (NMC). This rate is driven by the Total Non-Mission Capable for Maintenance, or TM rate and Total Non-Mission Capable for Supply, or TS rate.
STD: ≥ 99.30% Achieved: 99.90% as a YTD average and 99.86% QTD average.
TM Rate:
TM rate is a percentage of possessed or reported units unable to meet primary assigned missions for Fully Mission Capable for Maintenance (FMCM)+ Non-Mission Capable for Both (NMCB) divided by Possession Hours (POSS HRS).
STD: ≤ 3.80% Achieved: 1.31% as an YTD average and 1.79% QTD average.
TS Rate:
TS Rate is a percentage of possessed or reported units unable to meet primary assigned missions for supply reasons Non-Mission Capable for Supply (NMCS) plus Non- Mission Capable for Both (NMCB) divided by Possession Hours (POSS HRS).
STD: ≤ 5.50% Achieved: 0% as an YTD average and 0% QTD average.
Mean Time Between Failures:
Mean Time Between Failures is the Indication in Hours of system performance between malfunction that is Possession Hours divided by the Number of EVENTS.
STD: ≥ 424 HRS Achieved: 545 HRS as an YTD average and 526 HRS QTD average.
Mean Down Time:
Mean Down Time is the average number of hours to restore functionality that is Non-Mission Capable Maintenance divided by the number of EVENTS.
STD: ≤ 64 HRS Achieved: 13 HRS as an YTD average and 12 HRS QTD average.

## Slide 4
B-52H CE SCORECARD
Rate & STD | Avg | 1st Quarter 19 |  |  | QTD
MC | 98.70 | 99.91 |  |  | 99.91
TM | 6.40 | 0.43 |  |  | 0.43
TS | 0.40 | 0.00 |  |  | 0.00
MTBF | 24 | 39 |  |  | 39
MDT | 26 | 2 |  |  | 2
B-52 (AN/ASC-48) CE SCORECARD FY-19
2nd Quarter 19 |  |  | QTD
3rd Quarter 19 |  |  | QTD
4th Quarter 19 |  |  | QTD
YTD
99.91
0.43
0.40
39
2
- ARR-85 (MRT, LF/VLF)
- ARC-164 (UHF),
- ARC-190 (HF)
- ARC-210 (UHF/VHF)
- ASC-19 (UHF AFSATCOM)
Notes: B-52H NC3 Availability Chart
Scoreboard Indicators:
The combined B-52H Mission Capability rate takes into account the ARR-85, ARC-164, ARC-190, ARC-210 and ASC-19 individual systems.
The overall B-52H Configuration Element met 5 of 5 reported maintenance indicators for the Year To Date and Quarter To Date average . All standards were established by importing 24 months
of data into a standards development workbook, first up is the Mission Capability (MC) rate.
The monthly and quarterly data is color coded with either Green for Fully Mission Capable (FMC), Yellow for Partially Mission Capable (PMC), or Red for Non-Mission Capable (NMC). These color codes are categorized using the following parameters:
Green - At or less than 3% variance from the average
Yellow - Between 3-5% variance from the average
Red - Greater than 5% variance from the average
This goes for all categories except for Total Supply Downtime (TS), which use <10%, 10-15%, and >15% respectively.
MC Rate :
MC rate is a percentage that is either Fully Mission Capable (FMC) or Non-Mission Capable (NMC). This rate is driven by the Total Non-Mission Capable for Maintenance, or TM rate and Total Non-Mission Capable for Supply, or TS rate.
STD: ≥ 98.70% Achieved: 99.97% as an YTD average and 99.96% QTD average.
TM Rate:
TM rate is a percentage of possessed or reported units unable to meet primary assigned missions for Fully Mission Capable for Maintenance (FMCM)+ Non-Mission Capable for Both (NMCB) divided by Possession Hours (POSS HRS).
STD: ≤ 6.40% Achieved: .16% as an YTD average and .18% QTD average.
TS Rate:
TS Rate is a percentage of possessed or reported units unable to meet primary assigned missions for supply reasons Non-Mission Capable for Supply (NMCS) plus Non- Mission Capable for Both (NMCB) divided by Possession Hours (POSS HRS).
STD: ≤ 0.40% Achieved: 0% as an YTD average and 0% QTD average.
Mean Time Between Failures:
Mean Time Between Failures is the Indication in Hours of system performance between malfunction that is Possession Hours divided by the Number of EVENTS.
STD: ≥ 24 HRS Achieved: 147 HRS as an YTD average and 91 HRS QTD average.
Mean Down Time:
Mean Down Time is the average number of hours to restore functionality that is Non-Mission Capable Maintenance divided by the number of EVENTS.
STD: ≤ 26 HRS Achieved: 2 HRS as an YTD average and 2 HRS QTD average.

## Slide 5
B-2 CE SCORECARD
Rate | Avg | 1st Quarter 19 |  |  | QTD
MC | 98.20 | 99.95 |  |  | 99.95
TM | 5.30 | 0.20 |  |  | 0.05
TS | 0.30 | 0.00 |  |  | 0.00
MTBF | 72 | 128 |  |  | 128
MDT | 16 | 1 |  |  | 1
B-2 (AN/ASC-47) CE SCORECARD FY-19
2nd Quarter 19 |  |  | QTD
3rd Quarter 19 |  |  | QTD
4th Quarter 19 |  |  | QTD
YTD
99.95
0.20
0.00
128
1
- ARC-234 (UHF LOS)
- ARC-211 (HF)
- ASC-36 (UHF SATCOM)
Notes: B-2 NC3 Availability Chart
Scoreboard Indicators:
The combined B-2 Mission Capability rate takes into account the ARC-234, ARC-211 and ASC-36 individual systems.
Starting with the Lagging Indicators, the B-2 Configuration Element met 5 of 5 reported maintenance indicators for the Year To Date and Quarter To Date average. All standards were established by importing 24 months of data into a standards development workbook, first up is the Mission Capability (MC) rate.
The monthly and quarterly data is color coded with either Green for Fully Mission Capable (FMC), Yellow for Partially Mission Capable (PMC), or Red for Non-Mission Capable (NMC). These color codes are categorized using the following parameters:
Green - At or less than 3% variance from the average
Yellow - Between 3-5% variance from the average
Red - Greater than 5% variance from the average
This goes for all categories except for Total Supply Downtime (TS), which use <10%, 10-15%, and >15% respectively.
MC Rate :
MC rate is a percentage that is either Fully Mission Capable (FMC) or Non-Mission Capable (NMC). This rate is driven by the Total Non-Mission Capable for Maintenance, or TM rate and Total Non-Mission Capable for Supply, or TS rate.
STD: ≥ 98.20% Achieved: 99.96% as an YTD average and 99.99% as an QTD average.
TM Rate:
TM rate is a percentage of possessed or reported units unable to meet primary assigned missions for Fully Mission Capable for Maintenance (FMCM)+ Non-Mission Capable for Both (NMCB) divided by Possession Hours (POSS HRS).
STD: ≤ 5.30% Achieved: .12% as an YTD average and .02% as an QTD average.
TS Rate:
TS Rate is a percentage of possessed or reported units unable to meet primary assigned missions for supply reasons Non-Mission Capable for Supply (NMCS) plus Non- Mission Capable for Both (NMCB) divided by Possession Hours (POSS HRS).
STD: ≤ 0.30% Achieved: 0% as an YTD average and 0% as an QTD average.
Mean Time Between Failures:
Mean Time Between Failures is the Indication in Hours of system performance between malfunction that is Possession Hours divided by the Number of EVENTS.
STD: ≥ 72 HRS Achieved: 377 HRS as an YTD average and 676 HRS as an QTD average.
Mean Down Time:
Mean Down Time is the average number of hours to restore functionality that is Non-Mission Capable Maintenance divided by the number of EVENTS.
STD: ≤ 16 HRS Achieved: 2 HRS as an YTD average and 2 HRS as an QTD average.

## Slide 6
DCA (F-15E) CE SCORECARD
Rate | Avg | 1st Quarter 19 |  |  | QTD
MC | 99.80 | 99.9 |  |  | 99.9
TM | 0.30 | 0.30 |  |  | 0.30
TS | 0.50 | 0.50 |  |  | 0.50
MTBF | 102 | 102 |  |  | 102
MDT | 7 | 7 |  |  | 7
F-15E (AN/ASC-49) CE SCORECARD FY-19
2nd Quarter 19 |  |  | QTD
3rd Quarter 19 |  |  | QTD
4th Quarter 19 |  |  | QTD
YTD
99.99
0.30
0.50
102
7
- ARC-164(UHF)
- ARC-210 (UHF/VHF)
Notes: DCA (F15-E) NC3 Availability Chart
Scoreboard Indicators:
The combined DCA (F-15E) Mission Capability rate takes into account the ARC-164 and ARC-210 individual systems.
The DCA Configuration Element met 5 of 5 reported maintenance indicators for the Year To Date and Quarter To Date average . All standards were established by importing 24 months of data into a standards development workbook, first up is the Mission Capability (MC) rate.
The monthly and quarterly data is color coded with either Green for Fully Mission Capable (FMC), Yellow for Partially Mission Capable (PMC), or Red for Non-Mission Capable (NMC). These color codes are categorized using the following parameters:
Green - At or less than 3% variance from the average
Yellow - Between 3-5% variance from the average
Red - Greater than 5% variance from the average
This goes for all categories except for Total Supply Downtime (TS), which use <10%, 10-15%, and >15% respectively.
MC Rate :
MC rate is a percentage that is either Fully Mission Capable (FMC) or Non-Mission Capable (NMC). This rate is driven by the Total Non-Mission Capable for Maintenance, or TM rate and Total Non-Mission Capable for Supply, or TS rate.
STD: ≥ 99.80% Achieved: 99.99% as an YTD average and 99.98% as an QTD average.
TM Rate:
TM rate is a percentage of possessed or reported units unable to meet primary assigned missions for Fully Mission Capable for Maintenance (FMCM)+ Non-Mission Capable for Both (NMCB) divided by Possession Hours (POSS HRS).
STD: ≤ 0.30% Achieved: .02% as an YTD average and .04% as an QTD average.
TS Rate:
TS Rate is a percentage of possessed or reported units unable to meet primary assigned missions for supply reasons Non-Mission Capable for Supply (NMCS) plus Non- Mission Capable for Both (NMCB) divided by Possession Hours (POSS HRS).
STD: ≤ 0.50% Achieved: 0% as an YTD average and 0% as an QTD average.
Mean Time Between Failures:
Mean Time Between Failures is the Indication in Hours of system performance between malfunction that is Possession Hours divided by the Number of EVENTS.
STD: ≥ 102 HRS Achieved: 269 HRS as an YTD average and 266 HRS as an QTD average.
Mean Down Time:
Mean Down Time is the average number of hours to restore functionality that is Non-Mission Capable Maintenance divided by the number of EVENTS.
STD: ≤ 7 HRS Achieved: 1 HRS as an YTD average and 2 HRS as an QTD average.

## Slide 7
Airborne Support (U-2) CE SCORECARD
Rate | Avg | 1st Quarter 19 |  |  | QTD
MC | 99.90 | 99.94 |  |  | 99.94
TM | 0.04 | 0.08 |  |  | 0.08
TS | 0.13 | 0.00 |  |  | 0.00
MTBF | 165 | 134 |  |  | 134
MDT | 3 | 2 |  |  | 2
U-2 AN/ASC-50(V)3 CE SCORECARD FY-19
2nd Quarter 19 |  |  | QTD
3rd Quarter 19 |  |  | QTD
4th Quarter 19 |  |  | QTD
YTD
99.94
0.10
0.01
134
2
- ARC-217 (HF)
- ARC-210 (UHF/VHF)
Notes: Airborne Support (U-2) NC3 Availability Chart
Scoreboard Indicators:
The combined Airborne Support (U-2) Mission Capability rate takes into account the ARC-217 and ARC-210 individual systems.
The Airborne Support (U-2) Configuration Element met 5 of 5 reported maintenance indicators for the Year To Date and Quarter To Date average. All standards were established by importing 24 months of data into a standards development workbook, first up is the Mission Capability (MC) rate.
The monthly and quarterly data is color coded with either Green for Fully Mission Capable (FMC), Yellow for Partially Mission Capable (PMC), or Red for Non-Mission Capable (NMC). These color codes are categorized using the following parameters:
Green - At or less than 3% variance from the average
Yellow - Between 3-5% variance from the average
Red - Greater than 5% variance from the average
This goes for all categories except for Total Supply Downtime (TS), which use <10%, 10-15%, and >15% respectively.
MC Rate :
MC rate is a percentage that is either Fully Mission Capable (FMC) or Non-Mission Capable (NMC). This rate is driven by the Total Non-Mission Capable for Maintenance, or TM rate and Total Non-Mission Capable for Supply, or TS rate.
STD: ≥ 99.90% Achieved: 99.97% as an YTD average and 99.96% as an QTD average.
TM Rate:
TM rate is a percentage of possessed or reported units unable to meet primary assigned missions for Fully Mission Capable for Maintenance (FMCM)+ Non-Mission Capable for Both (NMCB) divided by Possession Hours (POSS HRS).
STD: ≤ 0.04% Achieved: 0.05% as an YTD average and 0.08% as an QTD average.
TS Rate:
TS Rate is a percentage of possessed or reported units unable to meet primary assigned missions for supply reasons Non-Mission Capable for Supply (NMCS) plus Non- Mission Capable for Both (NMCB) divided by Possession Hours (POSS HRS).
STD: ≤ 0.13% Achieved: 0% as an YTD average and 0% as an QTD average.
Mean Time Between Failures:
Mean Time Between Failures is the Indication in Hours of system performance between malfunction that is Possession Hours divided by the Number of EVENTS.
STD: ≥ 165 HRS Achieved: 284 HRS as an YTD average and 253 HRS as an QTD average.
Mean Down Time:
Mean Down Time is the average number of hours to restore functionality that is Non-Mission Capable Maintenance divided by the number of EVENTS.
STD: ≤ 3 HRS Achieved: 1 HRS as an YTD average and 2 HRS as an QTD average.

## Slide 8
ICBM CE SCORECARD
Rate | Avg | 1st Quarter 19 |  |  | QTD
MC | 97.1 | 95.7 | 94.7 |  | 95.2
TM | 6.1 | 3.3 | 3.9 |  | 3.6
TS | 0.2 | 1.3 | 0.0 |  | 0.6
MTBF | 300 | 327 | 264 |  | 296
MDT | 205 | 291 | 337 |  | 314
ICBM (AN/FSC-151V1) SCORECARD FY-20
2nd Quarter 19 |  |  | QTD
3rd Quarter 19 |  |  | QTD
4th Quarter 19 |  |  | QTD
YTD
95.2
3.6
0.6
296
314
- MMP-ET (EHF)
- MMP-VT (VLF/LF)
- FRC-175 (UHF MILSTAR)
- GRC-208 (UHF LOS)
Notes: ICBM NC3 Availability Chart
Good morning ???, I am Mr. ??? from the NC3 Center and I will be briefing the ICBM Configuration Element (CE) Maintenance Performance Indicators.
Scoreboard Indicators:
The combined NC3 Mission Capability rate takes into account MMP-EHF, MMP-VLF, FRC-175 UHF MILSTAR and GRC-208 UHF LOS. The ICBM CE met 4 of 5 reported maintenance indicators for the quarterly average and 4 of 5 for FY 20’s yearly average. The MC average was established by importing 36 months of data into an average development workbook.
The monthly and quarterly data is color coded with either Green for Fully Mission Capable (FMC), Yellow for Partially Mission Capable (PMC), or Red for Non-Mission Capable (NMC). These color codes are categorized using the following parameters:
Green - At or less than 3% variance from the average
Yellow - Between 3-5% variance from the average
Red - Greater than 5% variance from the average
This goes for all categories except for Total Supply Downtime (TS), which use <10%, 10-15%, and >15% respectively.
For the month of November, the ICBM CE accounted for 20 events, averaging totals just over 6,895 out of a possible 32.400 hours of total (maintenance, supply and deferred) downtime.
MC Rate : % that is either Fully Mission Capable, Partially Mission Capable, Non-Mission Capable
AVG: ≥97.1% Achieved: 95.2% as a YTD average and 95.2% QTD average
This rate is driven by the Total Non-Mission Capable for Maintenance (TNMCM) and Total Non-Mission Capable for Supply (TNMCS) rates.
TM Rate:
TM Rate is a percentage of possessed or reported units unable to meet primary assigned missions for Fully Mission Capable for Maintenance/Possession HRS
AVG: ≤6.1% Achieved: 3.6% as a YTD average and 3.6% as a QTD average.
TS Rate:
TS Rate is a percentage of possessed or reported units unable to meet primary assigned missions for supply reasons Non-Mission Capable for Supply/Possession HRS
AVG: ≤0.2% Achieved: 0.6% as a YTD average and a 0.6% as a QTD average.
Mean Time Between Failures: Indication in HRS of system performance between malfunction that is Possession HRS/# of EVENTS.
AVG: ≥300 HRS Achieved: 296 HRS as a YTD average and 296 HRS as a QTD average.
Mean Down Time: Average # of HRS to restore functionality, that is Non-Mission Capable for Maintenance/# of EVENTS.
AVG: ≤205 HRS Achieved: 314 HRS as a YTD average and 314 HRS as a QTD average. The reasoning behind the below average stat is addressed in the hyperlinked issue slide.

## Slide 9
Fixed Support CE SCORECARD
Rate | Avg | 1st Quarter 19 |  |  | QTD
MC | 86.80 | 100 | 100 | 89.49 | 96.50
TM | 8.2 | 0.00 | 0.00 | 15.46 | 5.15
TS | 22 | 0.00 | 0.00 | 5.57 | 1.86
MTBF | 478 | 744 | 720 | 472 | 645
MDT | 372 | 0 | 0 | 287 | 96
Fixed Support CE (AN/FSC-150) CE SCORECARD FY-19
2nd Quarter 19 |  |  | QTD
99.96 | 89.84 | 90.91 | 93.57
0.09 | 3.65 | 2.05 | 1.93
0.00 | 16.67 | 16.13 | 10.93
744 | 473 | 682 | 633
4 | 376 | 744 | 374
3rd Quarter 19 |  |  | QTD
95.35 | 88.21 | 92.96 | 92.18
6.57 | 5.39 | 14.08 | 8.68
2.73 | 18.18 | 0.00 | 6.97
525 | 518 | 517 | 520
184 | 482 | 279 | 315
4th Quarter 19 |  |  | QTD
99.95 | 96.87 | 89.68 | 95.50
0.10 | 6.26 | 10.63 | 5.66
0.00 | 0.00 | 10.00 | 3.33
744 | 489 | 506 | 580
4 | 85 | 409 | 166
YTD
94.44
5.36
5.77
594
238
- GRC-221 AACE (UHF LOS)
- FSC-125 SCAMP (EHF/SHF LDR SACTOM)
Notes: FIXED SUPPORT CE NC3 Availability Chart
Scoreboard Indicators:
The combined Fixed Support Mission Capability rate takes into account the GRC-221 AACE and FSC-125 SCAMP individual systems.
The Fixed Support Configuration Element met 5 of 5 reported maintenance indicators for the Year To Date and Quarter To Date average. All standards were established by importing 36 months of data into a standards development workbook. First up is the Mission Capability (MC) rate.
The monthly and quarterly data is color coded with either Green for Fully Mission Capable (FMC), Yellow for Partially Mission Capable (PMC), or Red for Non-Mission Capable (NMC). These color codes are categorized using the following parameters:
Green - At or less than 3% variance from the average
Yellow - Between 3-5% variance from the average
Red - Greater than 5% variance from the average
This goes for all categories except for Total Supply Downtime (TS), which use <10%, 10-15%, and >15% respectively.
MC Rate :
MC rate is a percentage that is either Fully Mission Capable (FMC) or Non-Mission Capable (NMC). This rate is driven by the Total Non-Mission Capable for Maintenance, or TM rate and Total Non-Mission Capable for Supply, or TS rate.
STD: ≥ 86.80% Achieved: 94.44% as an YTD average and a 95.50% QTD average.
TM Rate:
TM rate is a percentage of possessed or reported units unable to meet primary assigned missions for Non-Mission Capable for Maintenance (NMCM)+ Non-Mission Capable for Both (NMCB) divided by Possession Hours (POSS HRS).
STD: ≤ 8.2% Achieved: 5.36% as an YTD average and a 5.66% QTD average.
TS Rate:
TS Rate is a percentage of possessed or reported units unable to meet primary assigned missions for supply reasons Non-Mission Capable for Supply (NMCS) plus Non- Mission Capable for Both (NMCB) divided by Possession Hours (POSS HRS).
STD: ≤ 22.0% Achieved: 5.77% as an YTD average and a 3.33% QTD average.
Mean Time Between Failures:
Mean Time Between Failures is the Indication in Hours of system performance between malfunction that is Possession Hours divided by the Number of EVENTS.
STD: ≥ 478 HRS Achieved: 594 HRS as an YTD average and 580 HRS as a QTD average.
Mean Down Time:
Mean Down Time is the average number of hours to restore functionality that is Non-Mission Capable Maintenance divided by the number of EVENTS.
STD: ≤ 372 HRS Achieved: 238 HRS as an YTD average and 166 HRS as a QTD average. The last month of the quarter was RED with 409 HRS

## Slide 10
Questions?

## Slide 11: AIRBORNE U2 MEAN DOWN TIME
Issue: In FY-19, there was an average of 13 events logged per month, against an average of 134 hours between failures, out of 744 total monthly hours. Based on the high downtime hours average, the Mean Down Time rate was up significantly beyond the standard down time of 167 hours between failures.
Drivers were:
Antenna Pedestal Assembly (APA) outages
FRC-175 outages/ Transceiver Receiver (TR)
Impact: TX/RX capability
Way Ahead: The APA is a known issue trending up in the 2 months prior to MMPU deployment. The numbers were driven higher than normal due to extensive baseline testing of systems in preparation for deployment, creating a shortage in equipment and personnel…as deployment subsides, resources should become available. The FRC-175 (TR) was a victim of funding for higher priority resources, creating extended outages at two sites.
Contract Logistics Support: N/A
Start Date / Get Well Date: N/A
OCT-19 | NOV-19 | DEC-19 | Overall
Notes: FY19 average amount of maintenance events: 14
Number of events in September: 20
FY19 average of total downtime hours: 3653 hrs.
Amount of downtime hours in September: 8101 hrs.

## Slide 12: ICBM MEAN DOWN TIME
Issue: In November, there were 20 events logged, totaling 6895 hours of total (maintenance, supply, and deferred) downtime. Even with event amount being higher than the monthly average, the high downtime hours drove the Mean Down Time rate up significantly.
Critical drivers were:
6 Antenna Pedestal Assembly (APA) outages (3600 hrs.)
Impact: TX/RX capability
Way Ahead: The APA issue is a result of MMP Upgrade at 90 MW. Early in the deployment, baseline testing created concurrent multiple outages that normally would have surfaced over an extended period of time. This month’s outcome was anticipated as the repair system struggled to adjust to the additional load. Modifications in the baseline testing has since stemmed the flow of defective antennas, and is expected to bring down the APA down time as break rates return to normal. TSM issues at Minot related to training deficiencies, resolved; three (03) suspected defective batteries causing lack of sync and loss of TOD/WOD;. Not a trend, however, being monitored.
Contract Logistics Support: N/A
Start Date / Get Well Date: N/A
Oct-19 | Nov-19 | Dec-19 | Overall
Notes: FY19 average amount of maintenance events: 14
Number of events in November: 20
FY19 average of total downtime hours: 3653 hrs.
Amount of downtime hours in November: 6895 hrs.

## Slide 13: ICBM MEAN TIME BETWEEN FAILURES
Issue: In Quarter 4, there was an average of 18 events logged per month, against an average of 6381 hours of total (maintenance, supply, and deferred) downtime. Based on the higher than usual average events per month, the Mean Time Between Failures (MTBF) rate did not meet the standard for the quarter.
Frequent outage areas were:
MMP-ET outages (an average of 9 MMP-ET outages per month against what would normally be an average of 11 outages per month for all systems combined)
Impact: TX/RX capability
Way Ahead: The number of events were driven higher than normal due to extensive baseline testing of systems in preparation for MMPU deployment at 90 MW sites…consequently, this combined testing overtaxed the systems, identifying faults that normally would have surfaced over an extended period of time, all at once. Resumption of normal maintenance cycles, post MMPU deployment, should alleviate the issue.
Contract Logistics Support: N/A
Start Date / Get Well Date: N/A
Oct-19 | Nov-19 | Dec-19 | Overall
Notes: FY19 average amount of maintenance events: 14
Number of events in October: 18
FY19 average of total downtime hours: 3653 hrs.
Amount of downtime hours in October: 5715 hrs.

## Slide 14: Fixed Support CE MEAN DOWN TIME
Issue: In September two maintenance events occurred totaling 817 hours of maintenance and supply downtime. Due to the low number of events and the high amount of downtime, we exceeded our Mean Down Time standard of 372 hours by 37 hours.
Critical driver:
AACE was down for 407 hours due to a faulty Console Penetration Panel (CPP) Assy
Impact: TX/RX capability
Way Ahead: Beale’s AACE was down from 25 February to 17 September due to a faulty CPP. Beale sourced three panels outside of depot that were unserviceable. A fourth CPP sourced from depot arrived in September fixed the AACE. NG contract to repair unserviceable CPP assets is INWK. AFNC3C/NSP will continue to work with program office, depot and units to ensure serviceable parts are available and PQDRs are submitted.
Contract Logistics Support: N/A
Start Date / Get Well Date: N/A
Jul-19 | Aug-19 | Sept-19 | Overall